## Slide 1: ARIES: Path forward
Principal need:
Establish a common vision for what ARIES should look like in Phase I/II/III of MAPS. What are the science users’ expectation of ‘must-have’ capabilities?
  This will let us plan a realistic schedule, work with other programs for resources, and determine the real costs.
Given the change in landscape for high resolution IR spectroscopy over the last few years, are there changes to the work plan or the emergent capabilities?
  Talk of late has been focused on “adequate capabilities, delivered quickly” rather than a longer-term development.
  But what is “adequate”? And how soon is “quickly”? Need consensus from the MAPS users. Final thoughts, Jenny? (Or Katie: tell us what you want)
  Opinion: the key to doing this successfully is a focused “development campaign”.
  Development campaigns are (also) central to minimizing cost; “doing more with less”

## Slide 2: ARIES draft ”mission statement” for MAPS (key discussion points in red)
Supporting MAPS science with a baseline capability goal of:
Upgraded 1-5 um spectroscopy using a long-wave H2RG FPA, and existing electronics (at least initially)
Upgraded focal expander “zoom mode” to allow R=50K, over the default R=30K resolution
Upgraded “thru-slits” ala TripleSpec for better throughput, spectral resolution, fidelity (widths 0.1” to 0.4”)
Upgraded cross-dispersing prism design to support nodding along the slit at long wavelengths (e.g. better distribution of order separations)
Improved echelle grating mount to allow tip and tilt while cold, and with improved stability
Reduced instrument cryocooler microphonics (active vibration dampening)
While preserving existing low-resolution long-slit spectroscopic modes for non-MAPS science
And allowing for a more “facility-like” instrument installation, use, and data-processing pipeline, supported on a best-effort basis.
With the potential of an opportunity to:
Implement a higher resolution “R6” grating to support resolving powers of R=60K, and 100K in ‘zoom’ mode
Implement a more complete data processing pipeline and data archive
What else?