Science Objective	Science Measurement Requirement	Instrument Functional Requirement	Mission Functional Requirement	Compatwith OSIRIS
What is the H2O abundance and excitation in Galactic star forming regions?	Map H2O 110-101 over 100 degrees of the Galactic Plane.	At least one heterodyne mixer receiver at 557 GHz. Steerable antenna for pointing.	2 years of mapping during cruise phase(s), instrument must be able to see Galactic Plane.	??
	Spatially identify specific star forming regions: arcminute-scale angular resolution.	20 cm primary antenna yields 11' resolution	<10' pointing knowledge	??
	Velocity-resolve star forming clouds: 1 km/s velocity resolution.	Heterodyne receiver & digital spectrometer w/ 1 MHz channels. Generalized CPU for data reduction.	Instrument internal storage.	Yes
	Cover range of Galactic radial velocities, 300 km/s velocity range.	500 MHz IF bandwidth or steerable LO source w/ 250 MHz IF BW. Generalized CPU for data reduction.	800 b/s data rate for 500 chan & 0.1 Hz. Requires instrument internal storage.	Yes
	Sensitive to H2O abundances >10-6 : ability to detect TB<0.3 K	Trx(DSB)<2000K	Ambient temperature Schottky receivers	Yes
	Return 100 sq.deg. or equiv. Nyquist-sampled OTF maps.	>8 Gb internal storage, general purpose CPU for data reduction.	128 Mb of downlinked data	Yes
Is 1999 RQ36 a dead comet; does it outgas trace amounts of water, ammonia or carbon monoxide?	Detect H2O, NH3, CO absorption during mapping to N(H2O)<1010 cm-2	556-577 GHz tuning range. SNR>1000 toward continuum source (e.g. Sun or asteroid): Trx(DSB)<2000K	Requires limb sounding toward the Sun and/or long dwell times mapping the illuminated face of the asteroid. Absolute pointing <15'.	Yes?
What is the (sub)surface structure of 1999 RQ36?	Passive radiometry with SNR > 1000 toward asteroid surface.	Trx(DSB)<2000K, total power and/or spectroscopy measurements	Several days of mapping time.	Yes
Will the sample return process liberate subsurface water, ammonia, or carbon monoxide into the gas phase?	Detect H2O absorption in the “sample cloud” during TAG to N(H2O)<1010 cm-2. Active ranging & spectroscopy with SNR>1000	Trx(DSB)<2000K, DDS-scanning transceiver with >1mW power at 557 GHz	Permitted to operate during TAG maneuver, 30W power	Yes
	Return all asteroid data	>X Gb internal storage and onboard processing	XX Mb of downlinked data	??